	Virtual Machines	Linux Containers
RTT host ↔ VM | LXC / (min/mean/max/std.dev)	0.035/0.068/1.730/0.054 ms	0.005/0.007/0.110/0.003 ms
RTT VM↔VM | LXC ↔ LXC / (min/mean/max/std.dev)	0.072/0.152/3.441/0.110 ms	0.005/0.008/0.257/0.004 ms

		HAPROXY		NGINX		LVS
		VM	LXD	VM	LXD	VM	LXD
BAND- / WIDTH	iperf3	2.36 Gbps	9.63 Gbps	1.03 Gbps	8.32 Gbps	1.60 Gbps	27.7 Gbps
	iperf3 -R	8.83 Gbps	8.87 Gbps	8.07 Gbps	8.12 Gbps	3.62 Gbps	35.8 Gbps
	nuttcp	2.17 Gbps	8.01 Gbps	0.97 Gbps	9.01 Gbps	1.50 Gbps	20.75 Gbps
#REQ/ / SEC	ab	406.85	1731.05	508.32	1619.50	618.60	1770.05
	siege	141.90	767.29	187.57	719.93	212.40	648.78

Notes:

- See the annex at the end of this document for a brief explanation of the commands used.
- It’s important to notice that all tests are performed locally, on a laptop, and don’t traverse a network at all.
- With siege tests, virtual machines seem not able to handle more than 25 concurrent users (or at least the test takes a very long time). On the other hand Linux Containers handle up to 100 (probably more).
- Some tests might be biased because of caching mechanisms or CPU load/performance on the moment of the test.
- Not important differences found between round robin and least connections balancing modes. Maybe a more real scenario (Thredds with bigger datasets) would change that.
Scenario: haproxy_layer7 (VMs)

Test: ping -c 10000 -s 1472 -M do -i0 server-ip
Results:
RTT min/avg/max/mdev = 0.032/0.069/2.504/0.053 ms

Test: ab -n 10000 -c 100 load-bal-ip:8080/thredds/fileServer/collection1/singleDataset.nc
­Results:
Total time: 24.579 seconds
Request/sec: 406.85 #/sec (mean)
Time per request: 2.458 ms (mean)
Tranfer rate: ~ 21844.74 Kbytes/s

Connection Times (ms)
        min mean [+/-sd] median max
Connect: 0 1 14.6 0 1020
Processing: 5 245 205.3 217 2356
Waiting: 3 183 208.0 131 2305
Total: 5 245 205.9 217 2356

Percentage of the requests served within a certain time (ms)
  50% 217
  66% 236
  75% 253
  80% 278
  90% 384
  95% 503
  98% 721
  99% 1187
 100% 2356 (longest request)

Test: siege -b -i -r 100 -c 25
Results:
Transactions:	8003 hits
Availability:	100.00 %
Elapsed time:	56.40 secs
Data transferred:	54.94 MB
Response time:	0.16 secs
Transaction rate:	141.90 trans/sec
Throughput:	0.97 MB/sec
Concurrency:	22.73
Successful transactions: 8003
Failed transactions:	0

Test: iperf3 -c load-bal-ip
Results:
Bitrate: 2.36 Gbits/sec
Retries: 159

Test: nuttcp load-bal-ip
Results:
Bitrate: 2.17 Gbits/sec

Test: iperf3 -c load-bal-ip -R
Results:
Bitrate: 8.83 Gbits/sec
Retries: 0

Test: nuttcp -r load-bal-ip
Results:
Bitrate: --

Test: iperf3 -c server_ip
Results:
Bitrate: 2.33 Gbits/sec
Retries: 0

Test: nuttcp server-ip
Results:
Bitrate: 2.08 Gbits/sec

Test: iperf3 -c server_ip -R
Results:
Bitrate: 6.21 Gbits/sec
Retries: 0

Test: nuttcp -r server-ip
Results:
Bitrate: 6.26 Gbits/sec

Scenario: haproxy_lxd_containers

Test: ping -c 10000 -s 1472 -M do -i0 server-ip
Results:
RTT min/avg/max/mdev = 0.005/0.007/0.110/0.003 ms

Test: ab -n 10000 -c 100 load-bal-ip:8080/thredds/fileServer/collection1/singleDataset.nc
­Results:
Total time: 5.777 seconds
Request/sec: 1731.05 #/sec (mean)
Time per request: 0.578 ms (mean)
Tranfer rate: ~ 92944.02 Kbytes/s

Connection Times (ms)
        min mean[+/-sd] median max
Connect: 0 0 0.3 0 6
Processing: 1 57 66.9 37 581
Waiting: 1 53 66.5 31 580
Total: 1 57 66.9 37 581

Percentage of the requests served within a certain time (ms)
  50% 37
  66% 51
  75% 63
  80% 75
  90% 128
  95% 192
  98% 300
  99% 353
 100% 581 (longest request)

Test: siege -b -i -r 100 -c 100 (WITH ROUND ROBIN BALANCE MODE)
Results:
Transactions:	31835 hits
Availability:	100.00 %
Elapsed time:	41.49 secs
Data transferred:	219.66 MB
Response time:	0.12 secs
Transaction rate:	767.29 trans/sec
Throughput:	5.29 MB/sec
Concurrency:	92.77
Successful transactions: 31835
Failed transactions:	0
Longest transaction:	2.71
Shortest transaction:	0.00

Test: siege -b -i -r 100 -c 100 (WITH “LEAST CONNECTIONS” BALANCE MODE)
Results:
Transactions:	31708 hits
Availability:	100.00 %
Elapsed time:	49.19 secs
Data transferred:	220.06 MB
Response time:	0.14 secs
Transaction rate:	644.60 trans/sec
Throughput:	4.47 MB/sec
Concurrency:	92.58
Successful transactions: 31708
Failed transactions:	0

Test: iperf3 -c load-bal-ip
Results:
Bitrate: 9.63 Gbits/sec
Retries: 0

Test: nuttcp load-bal-ip
Results:
Bitrate: 8.01 Gbits/sec

Test: iperf3 -c load-bal-ip -R
Results:
Bitrate: 8.87 Gbits/sec
Retries: 1

Test: nuttcp -r load-bal-ip
Results:
Bitrate: --

Test: iperf3 -c server_ip
Results:
Bitrate: 40.7 Gbits/sec
Retries: 0

Test: nuttcp server-ip
Results:
Bitrate: 28.2 Gbits/sec

Test: iperf3 -c server_ip -R
Results:
Bitrate: 37.3 Gbits/sec
Retries: 0

Test: nuttcp -r server-ip
Results:
Bitrate: 27.65 Gbits/sec
Scenario: nginx (VMs)

Test: ping -c 10000 -s 1472 -M do -i0 server-ip (FROM HOST)
Results:
RTT min/avg/max/mdev = 0.032/0.069/2.607/0.060 ms

Test: ping -c 10000 -s 1472 -M do -i0 server-ip (FROM ANOTHER VM)
Results:
RTT min/avg/max/mdev = 0.072/0.152/3.441/0.110 ms

Test: ab -n 10000 -c 100 load-bal-ip:8080/thredds/fileServer/collection1/singleDataset.nc
­Results:
Total time: 19.673 seconds
Request/sec: 508.32 #/sec (mean)
Time per request:1.967 ms (mean)
Tranfer rate: 27290.28 Kbytes/s

Connection Times (ms)
        min mean[+/-sd] median max
Connect: 0 0 0.5 0 11
Processing: 6 195 66.5 189 693
Waiting: 5 192 64.9 187 692
Total: 6 196 66.4 189 693

Percentage of the requests served within a certain time (ms)
  50% 189
  66% 203
  75% 213
  80% 221
  90% 261
  95% 318
  98% 389
  99% 454
 100% 693 (longest request)

Test: siege -b -i -r 100 -c 25
Results:
Transactions:	7836 hits
Availability:	100.00 %
Elapsed time:	41.79 secs
Data transferred:	58.96 MB
Response time:	0.12 secs
Transaction rate:	187.51 trans/sec
Throughput:	1.41 MB/sec
Concurrency:	22.09
Successful transactions: 7836
Failed transactions:	0

Test: iperf3 -c load-bal-ip
Results:
Bitrate: 1.03 Gbits/sec
Retries: 2

Test: nuttcp load-bal-ip
Results:
Bitrate: 0.97 Gbits/sec

Test: iperf3 -c load-bal-ip -R
Results:
Bitrate: 1.20 Gbits/sec
Retries: 0

Test: nuttcp -r load-bal-ip
Results:
Bitrate: --

Test: iperf3 -c server_ip
Results:
Bitrate: 2.84 Gbits/sec
Retries: 153

Test: nuttcp server-ip
Results:
Bitrate: 2.53 Gbits/sec

Test: iperf3 -c server_ip -R
Results:
Bitrate: 8.07 Gbits/sec
Retries: 1

Test: nuttcp -r server-ip
Results:
Bitrate: 8.6 Gbits/sec
Scenario: nginx_lxd_containers

Test: ping -c 10000 -s 1472 -M do -i0 server-ip (FROM HOST)
Results:
RTT min/avg/max/mdev = 0.005/0.008/0.107/0.003 ms

Test: ping -c 10000 -s 1472 -M do -i0 server-ip (FROM ANOTHER CONTAINER)
Results:
RTT min/avg/max/mdev = 0.005/0.008/0.257/0.004 ms

Test: ab -n 10000 -c 100 load-bal-ip:8080/thredds/fileServer/collection1/singleDataset.nc
­Results:
Total time: 6.175 seconds
Request/sec: 1619.50 #/sec (mean)
Time per request:0.617 ms (mean)
Tranfer rate: 86946.77 Kbytes/s

Connection Times (ms)
        min mean[+/-sd] median max
Connect: 0 0 0.4 0 6
Processing: 1 61 58.0 46 611
Waiting: 0 60 57.7 45 611
Total: 1 61 58.0 46 611

Percentage of the requests served within a certain time (ms)
  50% 46
  66% 60
  75% 72
  80% 82
  90% 120
  95% 170
  98% 267
  99% 322
 100% 611 (longest request)

Test: siege -b -i -r 100 -c 100 (WITH ROUND ROBIN BALANCE MODE)
Results:
Transactions:	31612 hits
Availability:	100.00 %
Elapsed time:	43.91 secs
Data transferred:	224.46 MB
Response time:	0.13 secs
Transaction rate:	719.93 trans/sec
Throughput:	5.11 MB/sec
Concurrency:	91.42
Successful transactions: 31612
Failed transactions:	0
Longest transaction:	2.66
Shortest transaction:	0.00

Test: siege -b -i -r 100 -c 100 (WITH “LEAST CONNECTIONS” BALANCE MODE)
Results:
Transactions:	31721 hits
Availability:	100.00 %
Elapsed time:	41.71 secs
Data transferred:	219.93 MB
Response time:	0.12 secs
Transaction rate:	760.51 trans/sec
Throughput:	5.27 MB/sec
Concurrency:	91.48
Successful transactions: 31721
Failed transactions:	0

Test: iperf3 -c load-bal-ip
Results:
Bitrate: 8.32 Gbits/sec
Retries: 0

Test: nuttcp load-bal-ip
Results:
Bitrate: 9.01 Gbits/sec

Test: iperf3 -c load-bal-ip -R
Results:
Bitrate: 8.12 Gbits/sec
Retries: 1

Test: nuttcp -r load-bal-ip
Results:
Bitrate: --

Test: iperf3 -c server_ip
Results:
Bitrate: 41.1 Gbits/sec
Retries: 0

Test: nuttcp server-ip
Results:
Bitrate: 28.31 Gbits/sec

Test: iperf3 -c server_ip -R
Results:
Bitrate: 36.7 Gbits/sec
Retries: 1

Test: nuttcp -r server-ip
Results:
Bitrate: 28.16 Gbits/sec
Scenario: lvs_layer4 (VMs)

Test: ping -c 10000 -s 1472 -M do -i0 server-ip (FROM HOST)
Results:
RTT min/avg/max/mdev = 0.035/0.068/1.730/0.054 ms

Test: ping -c 10000 -s 1472 -M do -i0 server-ip (FROM ANOTHER VM)
Results:
RTT min/avg/max/mdev = 0.068/0.156/2.448/0.110 ms,

Test: ab -n 10000 -c 100 load-bal-ip:8080/thredds/fileServer/collection1/singleDataset.nc
­Results:
Total time: 16.165 seconds
Request/sec: 618.60 #/sec (mean)
Time per request: 1.617 ms (mean)
Tranfer rate: 33214.20 Kbytes/s

Connection Times (ms)
        min mean [+/-sd] median max
Connect: 0 0 0.6 0 8
Processing: 2 160 184.8 95 1129
Waiting: 1 118 121.4 80 919
Total: 3 161 184.9 96 1130

Percentage of the requests served within a certain time (ms)
  50% 96
  66% 178
  75% 230
  80% 267
  90% 424
  95% 577
  98% 722
  99% 804
 100% 1130 (longest request)

Test: siege -b -i -r 100 -c 100
Results:
Transactions:	7916 hits
Availability:	100.00 %
Elapsed time:	37.27 secs
Data transferred:	57.86 MB
Response time:	0.11 secs
Transaction rate:	212.40 trans/sec
Throughput:	1.55 MB/sec
Concurrency:	22.40
Successful transactions: 7916
Failed transactions:	0

Test: iperf3 -c load-bal-ip
Results:
Bitrate: 1.59 Gbits/sec
Retries: 669

Test: nuttcp load-bal-ip
Results:
Bitrate: 1.50 Gbits/sec

Test: iperf3 -c load-bal-ip -R
Results:
Bitrate: 3.62 Gbits/sec
Retries: 0

Test: nuttcp -r load-bal-ip
Results:
Bitrate: 5.26 Gbits/sec

Test: iperf3 -c server_ip
Results:
Bitrate: 2.19 Gbits/sec
Retries: 0

Test: nuttcp server-ip
Results:
Bitrate: 1.97 Gbits/sec

Test: iperf3 -c server_ip -R
Results:
Bitrate: 6.91 Gbits/sec
Retries: 0

Test: nuttcp -r server-ip
Results:
Bitrate: 5.57 Gbits/sec
Scenario: lvs_lxd_containers

Test: ping -c 10000 -s 1472 -M do -i0 server-ip
Results:
RTT min/avg/max/mdev = 0.005/0.007/0.110/0.003 ms

Test: ab -n 10000 -c 100 load-bal-ip:8080/thredds/fileServer/collection1/singleDataset.nc
­Results:
Total time: 5.650 seconds
Request/sec: 1770.05 #/sec (mean)
Time per request: 0.565 ms (mean)
Tranfer rate: 95038.05 Kbytes/s

Connection Times (ms)
        min mean[+/-sd] median max
Connect: 0 0 0.5 0 10
Processing: 1 56 64.8 32 594
Waiting: 1 41 49.8 24 533
Total: 1 56 64.8 32 594

Percentage of the requests served within a certain time (ms)
  50% 32
  66% 52
  75% 73
  80% 90
  90% 141
  95% 196
  98% 255
  99% 303
 100% 594 (longest request)

Test: siege -b -i -r 100 -c 100
Results:
Transactions:	32024 hits
Availability:	100.00 %
Elapsed time:	49.36 secs
Data transferred:	234.22 MB
Response time:	0.14 secs
Transaction rate:	648.78 trans/sec
Throughput:	4.75 MB/sec
Concurrency:	92.47
Successful transactions: 32024
Failed transactions:	0

Test: iperf3 -c load-bal-ip
Results:
Bitrate: 27.7 Gbits/sec
Retries: 394

Test: nuttcp load-bal-ip
Results:
Bitrate: 20.75 Gbits/sec

Test: iperf3 -c load-bal-ip -R
Results:
Bitrate: 35.8 Gbits/sec
Retries: 0

Test: nuttcp -r load-bal-ip
Results:
Bitrate: 26.51 Gbits/sec

Test: iperf3 -c server_ip
Results:
Bitrate: 40.7 Gbits/sec
Retries: 0

Test: nuttcp server-ip
Results:
Bitrate: 28.2 Gbits/sec

Test: iperf3 -c server_ip -R
Results:
Bitrate: 37.3 Gbits/sec
Retries: 0

Test: nuttcp -r server-ip
Results:
Bitrate: 27.65 Gbits/sec
Annex: Tests & Commands explanation

ping -c 10000 -s 1472 -M do -i0 server-ip

Sends 10,000 echo requests of maximum size with no fragmentation (1472 bytes) and no interval between them. As a result we obtain the Round Trip Time.

ab -n 10000 -c 100 load-bal-ip:8080/thredds/fileServer/collection1/singleDataset.nc

Performs 10,000 HTTP GET requests to the specified URL with the concurrency level specified by the -c option (i.e. in this case, 100 concurrent users performing each of them 100 consecutive requests). Most important results is #requests/second.

siege -b -i -r 100 -c 100

The number of concurrent users specified by the -c parameter perform the number of requests specified by the -r parameter (each of them). Option -b means benchmark mode which equals to zero seconds the interval between requests. -i option means Internet mode, hitting several URLs randomly amongst the URLs specified in a file located by default in /usr/local/etc/urls.txt
In this case this file contains the following URLs:

http://load-bal-ip:8080/thredds/catalog.html / http://load-bal-ip:8080/thredds/collection1/catalog.html / http://load-bal-ip:8080/thredds/collection1/sibling.html / http://load-bal-ip:8080/thredds/collection1/sibling.html?dataset=Dataset%201.1 / http://load-bal-ip:8080/thredds/fileServer/collection1/singleDataset.nc / http://load-bal-ip:8080/thredds/dodsC/collection1/singleDataset.nc.html / http://load-bal-ip:8080/thredds/ncss/collection1/singleDataset.nc/dataset.html / http://load-bal-ip:8080/thredds/fileServer/collection1/singleDataset.nc / http://load-bal-ip:8080/thredds/dodsC/collection1/singleDataset.nc.html / http://load-bal-ip:8080/thredds/ncss/collection1/singleDataset.nc/dataset.html / http://load-bal-ip:8080/thredds/collection2/catalog.html / http://load-bal-ip:8080/thredds/collection2/subcatalog/subcatalog.html / http://load-bal-ip:8080/thredds/collection2/subcatalog/subcatalog.html?dataset=Dataset%201.1

Siege accounts every request, including 301 Redirects and all items the page contains (.gif, css…) so that’s why the total number of requests doesn’t add up as concurrency X requests/user. Again, the most important result is the transaction rate.

iperf3 -c {dest-ip} [-R]

This command performs a bandwidth test between the host and {dest-ip} to achieve maximum bandwidth available. With the -R option the test is performed on reverse mode ({dest-ip} → host ). Bandwidth and loss rate are the important results here.

nuttcp -r {dest-ip}

Pretty much the same can be told about nuttcp as it has been said about iperf3.